## Slide 1: BOECQ DT EVEN Operation Scenario Specification EV
VER 1.2

## Slide 2: Specification Approval
Version | Name | Signature | Date | Description
1.2 | AIM |  | 2020-10-30 | BOECQ DT EVEN Operation Scenario Specification EV
Please sign below to indicate approval of this specification

## Slide 3: Revision History
Version | Date | author | Description
V 1.0 | 2020-09-28 | AIM | Initial Writing
V1.1 | 2020-10-21 | SINEVA | 1.add mask cassette type in the basic information. 2. add initial cleaner robot position. 3.modify unit number. 4.delete mask port's unit number. 5.modify glass transfer information. 6.modify loader & machine's job event flow. 7. Modify Port Number 8.add index port information in the index unit number definition
V1.2 | 2020-10-30 | AIM | Add Local#38 EGIS Modify Mask Port Scenario

## Slide 4: Contents
Part 1. Equipment Overview & Configuration
Part 2. Glass Flow
Part 3. Equipment Operation
Part 4. Data Collection
Part 5. Open Issue

## Slide 5: Sub Contents
Part 1. Equipment Overview & Configuration
1.1 System Configuration
1.2 Equipment Overview
1.3 Port Configuration
1.4 Equipment Layout
1.5 Indexer Robot Position Numbering
1.6 Unit Number Definition
1.7 Port Number Definition
1.8 Recipe Management
1.9 Glass Transfer Information

## Slide 6: 1.1 System Configuration
PLC and PC Configuration
Local No | Local#1 | Local#2 | Local#3 | Local#4 | Local#5 | Local#6 | Local#7 | Local#8 | Local#9 | Local#10 | Local#11 | Local#12 | Local#38
Machine | CIM-PC | Loader | ICLN | OVEN | Block0 | Block1 | Block3 | Block5 | Block7 | Block9 | BlockA | BlockC | EGIS
Vendor | AIM | 七星 |  | Hanwha | Tokki | Tokki | Tokki | Tokki | Tokki | Tokki | Tokki | Tokki | 
Comm Type | PLC HSMS | PLC | PLC | PLC | PLC | PLC | PLC | PLC | PLC | PLC | PLC | PLC | PLC
Sysmac:Local#1
CIM-PC
Local#5
Local#4
Local#3
Local#2
Local#6
Local#7
Local#31
Local#28
Local#27
Local#26
Local#25
PLC Type
PC Type
UTP Cable
Optical Cable
CC-Link IE Interface
Local#8
Local#9
Local#10
Local#11
Local#12
Local#13
Local#14
Local#15
Local#16
Local#17
Local#18
Local#19
Local#20
Local#21
Local#30
Local#29
HSMS Iterface
HSMS Communication Spec
Local#22
Local#23
Local#32
Local#33
Local#34
Local#35
Local#24
Local#36
Local#37
Line Network(Ethernet)
Local#38
Local#39

## Slide 7: 1.2 Equipment Overview
Basic Information
Item |  | Information | Description
Shop |  | EVEN | BP/EVEN/TSP/EAC/MOD
Equipment Type |  | Inline | Inline / Stand Alone
Local Qty |  | 37ea ( EV: 12ea, EN: 25 ) | EV Line : 12ea
Control Mode |  | Remote / Local / Offline | Remote / Local / Offline
Indexer Control Type |  | Dependent Type | Independent Type / Dependent Type
Indexer Port Qty |  | 8ea PL, 4ea PU | 4ea PL, 4ea PU
Port Type |  | PL, PU | PL(Load), PU(Unload), PB(Both)
Cassette Type |  | Half Glass Cassette, Mask Cassette | BP Glass Cassette, Half Glass Cassette, Film Cassette, 2 In 1 Cassette, Mask Cassette
Carrier Type |  | STK,MCT | STK, MGV
Buffer Qty |  | - | 
PLC Communication Spec. | H/W | CC-Link IE | Loader, EVEN Line
 | S/W | BOECQ DT_Equipment_Common_Communication_Specification | 
HSMS Communication Spec. | H/W | HSMS | CVD 1~4
 | S/W | BOECQ DT_Equipment_HSMS_Communication_Specification | 
LinkSignal Spec. | H/W | CC-Link IE | Loader, EVEN Line
 | S/W | BOECQ DT_Equipment_Link_Signal_Specification | 

## Slide 8: 1.3 Port Configuration
Port Properties of each Port for operations
Item | PL01 | PL02 | PL03 | PL04 | PL05 | PL06 | PL07 | PL08 | Description
Reader Type | RFR | RFR | RFR | RFR | RFR | RFR | RFR | RFR | BCR/RFR(RF-Reader)
Mapping Unit | Exist | Exist | Exist | Exist | Exist | Exist | Exist | Exist | Exist, Non Exist
Port Type | PL,PU | PL,PU | PL,PU | PL,PU | PL,PU | PL,PU | PL,PU | PL,PU | PL, PU, PB
Port Mode | OK, Dummy | OK, Dummy | OK, Dummy | OK, Dummy | OK, Dummy | OK, Dummy | OK, Dummy | OK, Dummy | OK, NG, Mix, Dummy
Cassette Type | Normal | Normal | Normal | Normal | Normal | Normal | Normal | Normal | Normal, A-Type, B-Type, Mask, Crate
Carrier Type | STK | STK | STK | STK | STK | STK | STK | STK | STK, MGV
Loading Container Condition | Actual/Empty | Actual/Empty | Actual/Empty | Actual/Empty | Actual/Empty | Actual/Empty | Actual/Empty | Actual/Empty | Empty : Container must be empty Actual : Container must be Actual Partial : Container must be Partial
Maximum Slot Number | 28 | 28 | 28 | 28 | 28 | 28 | 28 | 28 | 
Using Glass Kind | A-type or B-Type | A-type or B-Type | A-type or B-Type | A-type or B-Type | A-type or B-Type | A-type or B-Type | A-type or B-Type | A-type or B-Type | Glass / A-Type / B-Type

## Slide 9: 1.4 Equipment Layout
EQP Name | EV | EQP Type | Inline Type
Description for EQP Type | Dependent Type |  | 
Machine Name | Loader | ICLN | Oven | Block0 | Block1 | Block3 | Block5 | Block7 | Block9 | BlockA
Machine Name | BlockC |  |  |  |  |  |  |  |  | 

## Slide 10: 1.5 Indexer Robot Position Numbering
Number Assignment rule : The position number of the robot is given In/Out Station
Looking at the direction of the robot : right to left and bottom to up
In front of Port : 1 ~ 10
In front of Machine Stage : 11 ~ 20
Robot Position | Position Number
Home | 0
In front of Port | 1 ~ 10
In front of Machine Stage | 11 ~ 20
Reserved | 21 ~ 31
11
2
1
3
4
6
5
7
8
12

## Slide 11: 1.6 Unit Number Definition
Unit Configuration
Machine Status at Alarms
‘Position’ is a safety unit that prevents defects when congestion happens.
1
No | Description | Glass Qty | Max Glass Capacity | Position
1 | Indexer Robot Upper Arm | 1 | 226 | 1
2 | Indexer Robot Lower Arm | 1 |  | 2
- | Load Port1 | 28 |  | -
- | Load Port2 | 28 |  | -
- | Load Port3 | 28 |  | -
- | Load Port4 | 28 |  | -
- | Load Port5 | 28 |  | -
- | Load Port6 | 28 |  | -
- | Load Port7 | 28 |  | -
- | Load Port8 | 28 |  | -
2

## Slide 12: 1.6 Unit Number Definition
Unit Configuration
Machine Status at Alarms
‘Position’ is a safety unit that prevents defects when congestion happens.
ICLN
Turn
No | Description | Glass Qty | Max Glass Capacity | Position
1 | Input Conveyor | 1 | 16 | 1
2 | Buffer Conveyor | 1 |  | 2
3 | Extreme Ultraviolet | 1 |  | 3
4 | Roller Brush | 1 |  | 4
5 | HPMJ | 1 |  | 5
6 | Mix Jet | 1 |  | 6
7 | Final Rinse | 1 |  | 7
8 | Air Knife | 1 |  | 8
9 | Output Conveyor | 1 |  | 9
10 | Upper Transfer Conveyor | 7 |  | 10~16
1
2
3
4
5
6
7
8
9
10
ICLN

## Slide 13: 1.6 Unit Number Definition
Unit Configuration
Machine Status at Alarms
‘Position’ is a safety unit that prevents defects when congestion happens.
No | Description | Glass Qty | Max Glass Capacity | Position
1 | Transfer Robot01 | 1 | 70 | 1
2 | Transfer Robot02 | 1 |  | 2
3 | Revolve Robot | 1 |  | 3
4 | Load Lock01-Upper | 1 |  | 4
5 | Load Lock01-Lower | 1 |  | 5
6 | Load Lock02-Upper | 1 |  | 6
7 | Load Lock02-Lower | 1 |  | 7
8 | IR Oven01 | 16 |  | 8~23
9 | IR Oven02 | 16 |  | 24~39
10 | IR Oven03 | 16 |  | 40~55
11 | Cooling Buffer | 15 |  | 56~70
Oven
#2
ST
Oven
#1
Oven
#3
ST
1
2
3
ST
ST
4
5
6
7
8
9
10
11

## Slide 14: 1.6 Unit Number Definition
Unit Configuration
Machine Status at Alarms
‘Position’ is a safety unit that prevents defects when congestion happens.
ST
ST
ST
Block0
No | Description | Glass Qty | Max Glass Capacity | Position
1 | Load Chamber01 | 1 | 8 | 1
2 | Load Chamber02 | 1 |  | 2
3 | Transfer Robot00 Lower Arm | 1 |  | 3
4 | Transfer Robot00 Upper Arm | 1 |  | 4
5 | Plasma chamber0A | 1 |  | 5
6 | Plasma chamber0B | 1 |  | 6
7 | Plasma chamber0C | 1 |  | 7
8 | Plasma chamber0D | 1 |  | 8

## Slide 15: 1.6 Unit Number Definition
Unit Configuration
Machine Status at Alarms
‘Position’ is a safety unit that prevents defects when congestion happens.
ST
Block1
No | Description | Glass Qty | Max Glass Capacity | Position
1 | Buffer_Chamber01_Slot1 | 1 | 20 | 1
2 | Buffer_Chamber01_Slot2 | 1 |  | 2
3 | Buffer_Chamber01_Slot3 | 1 |  | 3
4 | Buffer_Chamber01_Slot4 | 1 |  | 4
5 | Buffer_Chamber01_Slot5 | 1 |  | 5
6 | Buffer_Chamber01_Slot6 | 1 |  | 6
7 | Buffer_Chamber01_Slot7 | 1 |  | 7
8 | Buffer_Chamber01_Slot8 | 1 |  | 8
9 | Turn_Chamber01 | 1 |  | 9
10 | Passage_Chamber01 | 1 |  | 10
11 | Transfer_Robot01_Lower_Arm | 1 |  | 11
12 | Transfer_Robot01_Upper_Arm | 1 |  | 12
13 | EV1A | 1 |  | 13
14 | EV1B | 1 |  | 14
15 | EV1C | 1 |  | 15
16 | EV1D | 1 |  | 16
17 | EV2A | 1 |  | 17
18 | EV2B | 1 |  | 18
19 | EV2C | 1 |  | 19
20 | EV2D | 1 |  | 20
No | Description | MaskQty | Max Mask Capacity | Position
- | Mask_stock1-1(Lower) | 5 | 20 | -
- | Mask_stock1-2(Upper) | 5 |  | -
- | Mask_stock2-1(Lower) | 5 |  | -
- | Mask_stock2-2(Upper) | 5 |  | -

## Slide 16: 1.6 Unit Number Definition
Unit Configuration
Machine Status at Alarms
‘Position’ is a safety unit that prevents defects when congestion happens.
ST
Block3
No | Description | Glass Qty | Max Glass Capacity | Position
1 | Passage_Chamber31 | 1 | 13 | 1
2 | Turn_Chamber03 | 1 |  | 2
3 | Passage_Chamber32 | 1 |  | 3
4 | Transfer_Robot03_Lower_Arm | 1 |  | 4
5 | Transfer_Robot03_Upper_Arm | 1 |  | 5
6 | EV3A | 1 |  | 6
7 | EV3B | 1 |  | 7
8 | EV3C | 1 |  | 8
9 | EV3D | 1 |  | 9
10 | EV4A | 1 |  | 10
11 | EV4B | 1 |  | 11
12 | EV4C | 1 |  | 12
13 | EV4D | 1 |  | 13
- | Mask stock3-1（Lower） | 5 | 20(Mask) | -
- | Mask stock3-2（Upper） | 5 |  | -
- | Mask stock3-3（Lower） | 5 |  | -
- | Mask stock3-4（Upper） | 5 |  | -

## Slide 17: 1.6 Unit Number Definition
Unit Configuration
Machine Status at Alarms
‘Position’ is a safety unit that prevents defects when congestion happens.
ST
Block5
No | Description | Glass Qty | Max Glass Capacity | Position
1 | Buffer_Chamber05_Slot1 | 1 | 20 | 1
2 | Buffer_Chamber05_Slot2 | 1 |  | 2
3 | Buffer_Chamber05_Slot3 | 1 |  | 3
4 | Buffer_Chamber05_Slot4 | 1 |  | 4
5 | Buffer_Chamber05_Slot5 | 1 |  | 5
6 | Buffer_Chamber05_Slot6 | 1 |  | 6
7 | Buffer_Chamber01_Slot7 | 1 |  | 7
8 | Buffer_Chamber05_Slot8 | 1 |  | 8
9 | Turn_Chamber05 | 1 |  | 9
10 | Passage_Chamber05 | 1 |  | 10
11 | Transfer_Robot05_Lower_Arm | 1 |  | 11
12 | Transfer_Robot05_Upper_Arm | 1 |  | 12
13 | EV5A | 1 |  | 13
14 | EV5B | 1 |  | 14
15 | EV5C | 1 |  | 15
16 | EV5D | 1 |  | 16
17 | EV6A | 1 |  | 17
18 | EV6B | 1 |  | 18
19 | EV6C | 1 |  | 19
20 | EV6D | 1 |  | 20
No | Description | MaskQty | Max Mask Capacity | Position
- | Mask_stock5-1(Lower) | 5 | 20 | -
- | Mask_stock5-2(Upper) | 5 |  | -
- | Mask_stock6-1(Lower) | 5 |  | -
- | Mask_stock6-2(Upper) | 5 |  | -

## Slide 18: 1.6 Unit Number Definition
Unit Configuration
Machine Status at Alarms
‘Position’ is a safety unit that prevents defects when congestion happens.
ST
Block7
No | Description | Glass Qty | Max Glass Capacity | Position
1 | Passage Chamber71 | 1 | 13 | 1
2 | Turn Chamber07 | 1 |  | 2
3 | Passage Chamber72 | 1 |  | 3
4 | Transfer Robot07 Lower Arm | 1 |  | 4
5 | Transfer Robot07 Upper Arm | 1 |  | 5
6 | EV7A | 1 |  | 6
7 | EV7B | 1 |  | 7
8 | EV7C | 1 |  | 8
9 | EV7D | 1 |  | 9
10 | EV8A | 1 |  | 10
11 | EV8B | 1 |  | 11
12 | EV8C | 1 |  | 12
13 | EV8D | 1 |  | 13
- | Mask stock7-1（Lower） | 5 | 20(Mask) | -
- | Mask stock7-2（Upper） | 5 |  | -
- | Mask stock7-3（Lower） | 5 |  | -
- | Mask stock7-4（Upper） | 5 |  | -

## Slide 19: 1.6 Unit Number Definition
Unit Configuration
Machine Status at Alarms
‘Position’ is a safety unit that prevents defects when congestion happens.
ST
Block9
No | Description | Glass Qty | Max Glass Capacity | Position
1 | Passage Chamber91 | 1 | 9 | 1
2 | Turn Chamber09 | 1 |  | 2
3 | Passage Chamber92 | 1 |  | 3
4 | Transfer Robot09 Lower Arm | 1 |  | 4
5 | Transfer Robot09 Upper Arm | 1 |  | 5
6 | EV9A | 1 |  | 6
7 | EV9B | 1 |  | 7
8 | EV9C | 1 |  | 8
9 | EV9D | 1 |  | 9
- | Mask stock9-1（Lower） | 5 | 10(Mask) | -
- | Mask stock9-2（Upper） | 5 |  | -

## Slide 20: 1.6 Unit Number Definition
Unit Configuration
Machine Status at Alarms
‘Position’ is a safety unit that prevents defects when congestion happens.
ST
BlockA
No | Description | Glass Qty | Max Glass Capacity | Position
1 | Buffer_Chamber0A_Slot1 | 1 | 16 | 1
2 | Buffer_Chamber0A_Slot2 | 1 |  | 2
3 | Buffer_Chamber0A_Slot3 | 1 |  | 3
4 | Buffer_Chamber0A_Slot4 | 1 |  | 4
5 | Buffer_Chamber0A_Slot5 | 1 |  | 5
6 | Buffer_Chamber0A_Slot6 | 1 |  | 6
7 | Buffer_Chamber0A_Slot7 | 1 |  | 7
8 | Buffer_Chamber0A_Slot8 | 1 |  | 8
9 | Turn_Chamber0A | 1 |  | 9
10 | Passage_Chamber0A | 1 |  | 10
11 | Transfer_Robot0A_Lower_Arm | 1 |  | 11
12 | Transfer_Robot0A_Upper_Arm | 1 |  | 12
13 | EVAA | 1 |  | 13
14 | EVAB | 1 |  | 14
15 | EVAC | 1 |  | 15
16 | EVAD | 1 |  | 16
- | Mask_stockA-1(Lower) | 5 | 10 | -
- | Mask_stockA-2(Upper) | 5 |  | -

## Slide 21: 1.6 Unit Number Definition
Unit Configuration
Machine Status at Alarms
‘Position’ is a safety unit that prevents defects when congestion happens.
BlockC
No | Description | Glass Qty | Max Glass Capacity | Position
1 | Passage_ChamberC1 | 1 | 10 | 1
2 | Turn_Chamber0C | 1 |  | 2
3 | Passage_ChamberC2 | 1 |  | 3
4 | Transfer_Robot0C_Lower_Arm | 1 |  | 4
5 | Transfer_Robot0C_Upper_Arm | 1 |  | 5
6 | EVCA | 1 |  | 6
7 | EVCB | 1 |  | 7
8 | EVCC | 1 |  | 8
9 | EVCD | 1 |  | 9
10 | Passage_ChamberC3 | 1 |  | 10
- | Mask stockC-1（Lower） | 1 | 10(Mask) | -
- | Mask stockC-2（Upper） | 1 |  | -

## Slide 22: 1.7 Port Number Definition
Number Assignment Rule : From stocker looking at the direction, left to right and bottom to up
2
1
3
4
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
6
5
7
8

## Slide 23: 1.8 Recipe Management
Equipment Common Operation Scenario
[ CIMPC Client Display ]
[ Refer to Recipe Management in the Equipment Common Operation Scenario ]
CIM PC download PPID to Loader. Job data include PPID.
All equipment should provide automatic recipe change function.
Different kind of product can not be mixed in one local equipment.
All equipment should provide auto recipe change function. Equipment should provide auto recipe change enable / disable change function on equipment
touch panel.
a. Enable: Equipment should change Recipe ID by automatic.
b. Disable: Equipment should change Recipe ID by manual.
Different kind of product can be loaded at the same time in loader.
Dummy also need recipe management.
MES
CIM-PC
LOADER
Host PPID (BOE-32T-PPID1)
Equipment
Un-Loader
[ Recipe Management ]
Job data include PPID
Job Data
Include PPID
Job Data
Include PPID
No | Host PPID | Recipe Number |  |  | 
 |  | L1 | L2 | L3 | L4
1 | BOE-32T-PPID1 | AA9999 | PI1000 | 1000 | MP9999
2 | BOE-32T-PPID2 | AD1111 | PI1500 | 1111 | MP9999
… |  | … |  | … | …
300 | BOE-32T-PPIDn | AG5555 | PM1000 | 5555 | MP9999
PPID = AA9999 PI1000 __1000 MP9999
L1 recipe
L2 Recipe
L3 recipe
1 words ASCII +
1 words Integer
L4 recipe
Equipment Recipe
Current Recipe No. | AA9999
Recipe Register Table
Recipe No. | Glass Size | Process Temp | Process Pressure | Etc
AA9999 | 1300*1100 | 45 | 100 | …
AB1111 | 1300*1100 | -45 | 50 | …
… | … | … | … | …
*If Not use ASCII,
ASCII value is Space(32).
Ex) 1000

## Slide 24: 1.8 Recipe Management
Recipe Position Assign
[ Recipe – Local Position Assign ]
Position | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Local No | L3 | L4 | L5 | L6 | L7 | L8 | L9 | L10 | L11 | L12 | L17 | L18
EQ Name | ICLN | OVEN | Block0 | Block1 | Block3 | Block5 | Block7 | Block9 | BlockA | BlockC | SE | LO
Position | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Local No | L19 | L20 | L21 | L22 | L23 | L24 | L26 | L28 | L29 | L30 | L31 | L32
EQ Name | OM | AOI1 | CVD1 | CVD2 | TM5 | IJP | IJP AOI | Aging Oven | CVD3 | CVD4 | TFE SE | AOI2
Position | 25 | 26 |  |  |  |  |  |  |  |  |  | 
Local No | L33 |  |  |  |  |  |  |  |  |  |  | 
EQ Name | AOI3 |  |  |  |  |  |  |  |  |  |  | 
PPID = AA9999 PI1000 __1000 …. BB9999
L1 recipe
L2 Recipe
L3 recipe
1 words ASCII +
1 words Integer
….
L33 recipe

## Slide 25: 1.8 Recipe Management
Recipe Parameter Management
CIM PC Request “Recipe Parameter Check” to EQ when MES request recipe parameter
- key : Line ID, EQID, Recipe ID
EQ Reply Recipe parameter to CIM PC
CIM PC report this parameter to MES
Parameter ID | Parameter Name | Recipe Type | Machine ID /Unit ID | Recipe Step Number | Recipe Value | Min Recipe Value | Max Recipe Value | Value Unit (SI) | Format | Length (Word) | Description
1 | ParameterName1 | Machine Recipe | Machine#1 | 1 | 35 | 1 | 99 | °C | Unsigned Integer | 2 Word | Temperature
2 | ParameterName2 | Machine Recipe | Machine#2 | 2 | 10 | 1 | 99 | MPa | Float | 2 Word | Pressure
3 | ParameterName3 | Unit Recipe | Machine#1-Unit#1 | 1 | 35 | 1 | 99 | °C | Signed Integer | 2 Word | Temperature
4 | ParameterName4 | Unit Recipe | Machine#1-Unit# | 2 | 10 | 1 | 99 | MPa | ASCII | 2 Word | Pressure
….. | …. | … | … | …. | … | … | … | …. | … | … | …
65534 | ParameterName 65534 | Machine Recipe | Machine#1 | 2 | 10 | 1 | 99 | MPa | Float | 2 Word | Pressure
65535 | ParameterName 65535 | Unit Recipe | Machine#1-Unit#2 | 3 | 10 | 1 | 99 | MPa | Unsigned Integer | 2 Word | Pressure

## Slide 26: 1.8 Recipe Management
DownStream
Machine
CIM-PC
UpStream
Machine
Writing JOB data
Auto Recipe Change Mode
ReceiveAble On
SendAble On
Read
JOB data
Parsing RecipeID
If necessary, Setup the received recipe
Recipe Change Report
ReceiveStart On
Glass Transfer
ReceiveComplete On
Process Start
Process Start Report
[Normal Case]
DownStream
Machine
CIM-PC
UpStream
Machine
Writing JOB data
ReceiveAble On
SendAble On
Read
JOB data
Recipe Not Registered
[AbNormal Case – Recipe Not Registered at Machine]
OPCALL
Register Recipe
OPCALL Clear
Writing JOB data
ReceiveAble On
SendAble On
Read
JOB data
Continue Normal Case

## Slide 27: 1.8 Recipe Management
Recipe Register Validation
Machine
CIM-PC
Indexer
Cassette Load Complete
RMS
Cassette Info. Request
Validation Check
Cassette Info. Update
Cassette Info. Send
Job Start Command Send
Job Start Command
Recipe Register Check Command
Recipe Register Check
(Machine)
(Unit)
…
Recipe ID Check timing : CST on Port
CIM PC Request “Recipe Register Validation” to EQ
EQ compare EQ’s registered Recipe and download Recipe from CIM PC
EQ reply to CIMPC
- ACK : All exist (can process)
- NACK : not matched at least one
(cannot Process)
Unit Number≠0
Block | Item Name | Type | Length
Recipe Register Check Command Send Block | Recipe Text | ASCII | 1
 | Recipe Number | INT | 1
 | Unit Number | INT | 1
Recipe Text: 2 characters (If not use, Fill Space(H20))
Recipe Number: 1~9999 (0 is default Cold Run)
Unit Number : If there is no Unit Recipe then 0
Recipe Register Check
(Machine)
(Unit)
…
Recipe Register Check Command
Recipe Register Check Command Reply Pass
Recipe Register Check Command Reply Pass
Unit Number=0

## Slide 28: 1.8 Recipe Management
Recipe Change Report
Machines report ‘Recipe Change Report’ when it occurs.
CIM-PC
RMS
Machine
Recipe Change Report
[Machine CIM-PC : Recipe Change Report]
Type | Name | Data Type | Value Type | Length
Recipe Change Report Block | Recipe Change Type | WORD | INT | 1
 | Recipe Version Sequence Number | WORD | INT | 1
 | Operator ID | WORD | INT | 10
 | Unit Number | WORD | INT | 1
 | Recipe Text | WORD | ASCII | 1
 | Recipe Number | WORD | INT | 1
Recipe Change Type : 1-Generate, 2-Edit, 3-Delete
Recipe Parameter Change
Recipe Change Type
Recipe Parameter Request Command Send
Recipe Parameter Request Command Send Reply
Unit Number
[CIM-PC → Machine : Recipe parameter Request]
Type | Name | Data Type | Value Type | Length
Recipe Parameter Request Block | Recipe Text | WORD | ASCII | 1
 | Recipe Number | WORD | INT | 1
 | Unit Number | WORD | INT | 1
 | Recipe Step Number | WORD | INT | 1
Type | Name | Data Type | Value Type | Length
Recipe Parameter Request Reply Block | Recipe Text | WORD | ASCII | 1
 | Recipe Number | WORD | INT | 1
 | Recipe Version Sequence Number | WORD | INT | 1
 | Unit Number | WORD | INT | 1
 | Recipe Step Number | WORD | INT | 1
 | Result | WORD | INT | 1
 | Parameter Value #1 | WORD | TBD | TBD
 | ... |  |  | 
 | Parameter Value #N | WORD | TBD | TBD
[CIM-PC ← Machine : Recipe parameter reply]
Unit Number: Number of Unit recipe, if not Unit recipe, set 0 (0 means Machine)
Recipe Parameter Change Report
Recipe Parameter Change
Recipe Change Type :
1-Generate
2-Edit
3-Delete
Unit Number:
0-Machine
1-Unit#1
2-Unit#2
⁞
Case1 :When Machine is CIM On

## Slide 29: 1.8 Recipe Management
Recipe Change Report
Machines report ‘Recipe Change Report’ when it occurs.
CIM-PC
RMS
Machine
Recipe1 Change Report
Recipe Parameter Request Command Send
Recipe Parameter Request Command Send Reply
…
Recipe Parameter Change Report
Recipe Parameter Change
Case2 :When Machine is CIM Off
Recipe1 Para. Change
…
RecipeN Para. Change
CIM Off
CIM On
RecipeN Change Report
Recipe Parameter Request Command Send
Recipe Parameter Request Command Send Reply
…
Recipe Parameter Change Report
Recipe Parameter Change
If Recipe Parameter is Changed by user when Machine is CIM Off, Machine should keep the change history and report Parameter change to CIM when Machine is CIM On.
If more than 1 recipe are changed, Machine should report recipe parameter change report one by one, and machine should keep at least 0.5 second time delay(T3 Timeout) between each report.

## Slide 30: 1.8 Recipe Management
Recipe Step
CIMPC can request machine recipe’s Step Count Information from process machines. When CIMPC request recipe’s Step Count Information, machine should reply recipe’s Step Count Information of corresponding Recipe Number
CIM-PC
RMS
Machine
[CIM-PC  Machine : Recipe Step Count Request]
Type | Name | Data Type | Value Type | Length
Recipe Step Count Request Block | Recipe Text | WORD | ASCII | 1
 | Recipe Number | WORD | INT | 1
 | Unit Number | WORD | INT | 1
Recipe Step Count Request
Recipe Step Count
Recipe Step Count Request Reply
Recipe Step Count Update
[Machine  CIMPC : Recipe Step Count Request Reply]
Type | Name | Data Type | Value Type | Length
Recipe Step Count Request Reply Block | Recipe Text | WORD | ASCII | 1
 | Recipe Number | WORD | INT | 1
 | Unit Number | WORD | INT | 1
 | Recipe Version Sequence Number | WORD | INT | 1
 | Step Count | WORD | INT | 1
PP_BODY Check (Step)
PP_BODY Check Reply (Step)

## Slide 31: 1.8 Recipe Management
Recipe Parameter Request
CIM-PC
RMS
Machine
Request Recipe Para.
(Machine)
Request Recipe Step Count
(Machine)
Step Count Update
Parameter Request
Parameter Update
Step Count Request
Machine Recipe
Request Recipe Para.
Recipe Para. Reply
Recipe Para. Reply (Machine)
Reply Recipe Parameter
Operators(RMS) request Machine Recipe Parameter Value
[CIM-PC → Machine : Recipe parameter Request]
Type` | Name | Data Type | Value Type | Length
Recipe Parameter Request Block | Recipe Text | WORD | ASCII | 1
 | Recipe Number | WORD | INT | 1
 | Unit Number | WORD | INT | 1
 | Recipe Step Number | WORD | INT | 1
[CIM-PC ← Machine : Recipe parameter reply]
Unit Number: Number of Unit recipe, if not Unit recipe, set 0 (0 means Machine)
Recipe Step Count Request
Recipe Step Count Request Reply Count=1
Step Count(1) Update
Request Recipe Step Count
Step Count Reply
Unit Number=0
If there no Recipe step then Step Number is 1 ( Default is 1 )
Type | Name | Data Type | Value Type | Length
Recipe Parameter Request Reply Block | Recipe Text | WORD | ASCII | 1
 | Recipe Number | WORD | INT | 1
 | Recipe Version Sequence Number | WORD | INT | 1
 | Unit Number | WORD | INT | 1
 | Recipe Step Number | WORD | INT | 1
 | Result | WORD | INT | 1
 | Parameter Value #1 | WORD | TBD | TBD
 | ... |  |  | 
 | Parameter Value #N | WORD | TBD | TBD

## Slide 32: 1.8 Recipe Management
Recipe Parameter Download (Machine Recipe, By RMS)
CIM-PC
RMS
Machine
Recipe Parameter Change Cmd.
Recipe Step No.
Recipe Parameter Change Command
If acceptable, Change Recipe Parameter
Reply Ack
Recipe Parameter Change Rep.
Reply results
Recipe Para. Download
Recipe Parameter Change Command
[CIM-PC  Machine : Recipe Parameter Data Download]
[Machine CIM-PC : Acknowledge for Recipe Parameter Change]
Type | Name | Data Type | Value Type | Length
Recipe Parameter Data Download Send Block | Recipe Text | WORD | ASCII | 1
 | Recipe Number | WORD | INT | 1
 | Unit Number | WORD | INT | 1
 | Recipe Step Number | WORD | INT | 1
 | Parameter Value #1 | WORD | TBD | TBD
 | ... |  |  | 
 | Parameter Value #N | WORD | TBD | TBD
1.
Unit Number: Number of Unit recipe, if not Unit recipe, set 0 (0 means Machine)
Type | Name | Data Type | Value Type | Length
Recipe Parameter Data Download Reply Block | Recipe Parameter Data Download Result | WORD | INT | 1
Recipe Parameter Data Download Result Code
1 : Accepted
2 : Not Accepted – Recipe not exist
3 : Not Accepted – Recipe being used
4: Not Accepted – Validation NG (ex, out of range)
[Machine CIM-PC : Recipe Change Report]
Type | Name | Data Type | Value Type | Length
Recipe Change Report Block | Recipe Change Type | WORD | INT | 1
 | Recipe Version Sequence Number | WORD | INT | 1
 | Operator ID | WORD | INT | 10
 | Unit Number | WORD | INT | 1
 | Recipe Text | WORD | ASCII | 1
 | Recipe Number | WORD | INT | 1
Recipe Change Type : 1-Generate, 2-Edit, 3-Delete
Recipe Change Type=2
Recipe Parameter Request Command Send
Recipe Parameter Request Command Send Reply
Unit Number=0 Recipe Step No.
Recipe Change Report
Repeat by Step Quantity
Parameter Change
Unit Number=0 Recipe Step No.
Unit Number=0 Recipe Step No.
(Machine)

## Slide 33: 1.9 Glass Transfer Information
Transfer Information
1
3
4
5
9
2
No | From (UpStream) |  |  |  | To (DownStream) |  |  |  | LinkSignal Type
 | Local No | EQ Type | Slot | Upstream Path No | Local No | EQ Type | Slot | Downstream Path No | 
1 | L2 | Double Arm | 1 | 1 | L3 | Single Stage | 1 | 1 | 2
2 | L3 | Single Stage | 1 | 2 | L2 | Double Arm | 1 | 1 | 8
3 | L3 | Convey | 1 | 1 | L4 | Double Arm | 1 | 1 | 8
4 | L4 | Double Arm | 1 | 1 | L5 | Single Stage | 1 | 1 | 4
5 | L4 | Double Arm | 1 | 2 | L5 | Single Stage | 1 | 2 | 4
6 | L5 | Single Stage | 1 | 1 | L4 | Double Arm | 1 | 2 | 10
7 | L5 | Single Stage | 1 | 2 | L4 | Double Arm | 1 | 3 | 10
6
7
8
10

## Slide 34: 1.9 Glass Transfer Information
Transfer Information
9
No | From (UpStream) |  |  |  | To (DownStream) |  |  |  | LinkSignal Type
 | Local No | EQ Type | Slot | Upstream Path No | Local No | EQ Type | Slot | Downstream Path No | 
8 | L4 | Double Arm | 1 | 1 | L3 | Convey | 1 | 1 | 2
9 | L12 | Single Stage | 1 | 1 | L13 | Double Arm | 1 | 1 | 10
10 | L12 | Single Stage | 1 | 2 | L13 | Double Arm | 1 | 2 | 10
8

## Slide 35: Sub Contents
Part 2. Equipment Overview & Configuration
2.1 Glass Flow
2.2 Flow Type
2.3 Job Event

## Slide 36: 2.1 Glass Flow
Glass Flow
No | Category | Flow Type | Subject | Description
1 | Normal Flow | Process All | All Process | CST → Initial Cleaner → Oven → Block0 → Block1 → Block3 → Block5 → Block7 → Block9 → BlockA → BlockC
2 | Normal Flow – Key Glass | Key Glass Normal Mode | Key Glass – All Process | CST → Initial Cleaner → Oven → Block0 → Block1 → Block3 → Block5 → Block7 → Block9 → BlockA → BlockC
3 | Mix Run Flow | Mix Run Flow | All Process | Recipe A : CST → Initial Cleaner → Oven → Block0 ( Route A )→ Block1 ( Route A ) → Block3 ( Route A ) → Block5 ( Route A ) → Block7 ( Route A ) → Block9 ( Route A ) → BlockA ( Route A ) → BlockC ( Route A ) Recipe B : CST → Initial Cleaner → Oven → Block0 ( Route B )→ Block1 ( Route B ) → Block3 ( Route B ) → Block5 ( Route B ) → Block7 ( Route B ) → Block9 ( Route B ) → BlockA ( Route B ) → BlockC ( Route B )
4 | Mix Run Flow – Key Glass | Key Mix Run Flow | Key Glass – All Process | Recipe A and A Key Glass : CST → Initial Cleaner → Oven → Block0 ( Route A )→ Block1 ( Route A ) → Block3 ( Route A ) → Block5 ( Route A ) → Block7 ( Route A ) → Block9 ( Route A ) → BlockA ( Route A ) → BlockC ( Route A ) Recipe B and B Key Glass : CST → Initial Cleaner → Oven → Block0 ( Route B )→ Block1 ( Route B ) → Block3 ( Route B ) → Block5 ( Route B ) → Block7 ( Route B ) → Block9 ( Route B ) → BlockA ( Route B ) → BlockC ( Route B )
5 | Cold Run Flow | Cold Run Flow | All Process Skip | Machine Mode : Cleaner Only Cold Run Mode Flow By Skip Recipe : Flow by Initial Cleaner Only Cold run Recipe, Cleaner Machine Process Skip Glass Flow : Cassette -> Robot -> Initial Cleaner -> Robot -> Cassette
6 | Cold Run Flow | Initial Cleaner Only Cold Run | Initial Cleaner Skip | Machine Mode : Cleaner Only Cold Run Mode Flow By Skip Recipe : Flow by Initial Cleaner Only Cold run Recipe, Cleaner Machine Process Skip Glass Flow : Cassette -> Robot -> Initial Cleaner -> Robot -> Cassette

## Slide 37: 2.1 Glass Flow
Glass Flow
No | Category | Flow Type | Subject | Description
7 | Dummy Flow | EN Dummy Flow | All Process Skip | Glass Flow : CST → Cleaner → Oven( Process Unit By Pass ) → Block0 ~BlockC ( Process Unit By Pass ) → TM1(EN Line)
8 | Abnormal Flow | IR Oven Reverse Flow | All Process Skip | Machine Mode : Manual Mode Flow By Machine Mode : This Mode Only Can use Semi Auto, If the block machine is down for a long time, the glass in the cooling buffer is returned back to the loader port. Glass Flow : Cooling Buffer -> Oven TM -> Initial Cleaner -> Robot -> Cassette
 |  | Mix Run Flow | All Process | Recipe A : CST → Initial Cleaner → Oven → Block0 ( Route A )→ Block1 ( Route A ) → Block3 ( Route A ) → Block5 ( Route A ) → Block7 ( Route A ) → Block9 ( Route A ) → BlockA ( Route A ) → BlockC ( Route A ) Recipe B : CST → Initial Cleaner → Oven → Block0 ( Route B )→ Block1 ( Route B ) → Block3 ( Route B ) → Block5 ( Route B ) → Block7 ( Route B ) → Block9 ( Route B ) → BlockA ( Route B ) → BlockC ( Route B )
 |  | Initial Cleaner Mismatching Recipe Flow | All Process Skip | Machine Mode : Manual Mode Flow By Recipe : If recipe of the inserted glass does not match, Glass Back to the Loader Glass Flow : CST → Robot → Cleaner → Robot → CST
 |  | Machine & Process Skip | All Process | Force Clean Out Mode

## Slide 38: 2.1 Glass Flow
Normal Flow
CIM PC Mode : Normal Mode
Machine Mode : Normal Mode
1. Flow By Recipe
2. Glass Flow
: CST → Initial Cleaner → Oven → Block0 → Block1 → Block3 → Block5 → Block7 → Block9 → BlockA → BlockC
※ If necessary, Block 0 Machine can requests Route Recipe Number to CIM
: Normal Glass
: Process Skip

## Slide 39: 2.1 Glass Flow
Normal Flow - Key Glass
CIM PC Mode : Key Glass Normal Mode
Machine Mode : Normal Mode
Job Change Flag
: This flag must be defined before the Cassette is loaded into the Port, and CIM Insert the defined key glass when the job change flag is detected
Recipe A
Key Recipe
: Recipe A Flow
: Recipe B Flow
: Key Recipe Flow
Start
Job Change Flag is On
Get A Recipe
Get Key Recipe

## Slide 40: 2.1 Glass Flow
Mix Run Flow
Recipe A
Recipe B
CIM PC Mode : Mix Run Mode
Machine Mode : Multi Mix Run Mode
1. Flow By Recipe
2. Glass Flow
Recipe A : CST → Initial Cleaner → Oven → Block0 ( Route A )→ Block1 ( Route A ) → Block3 ( Route A ) → Block5 ( Route A ) → Block7 ( Route A ) → Block9 ( Route A ) → BlockA ( Route A ) → BlockC ( Route A )
Recipe B : CST → Initial Cleaner → Oven → Block0 ( Route B )→ Block1 ( Route B ) → Block3 ( Route B ) → Block5 ( Route B ) → Block7 ( Route B ) → Block9 ( Route B ) → BlockA ( Route B ) → BlockC ( Route B )
※ If necessary, Block 0 Machine can requests Route Recipe Number to CIM
: Recipe A Flow
: Recipe B Flow

## Slide 41: 2.1 Glass Flow
Mix Run Flow - Key Glass
CIM PC Mode : Key Mix Run Mode
1) Job Change flag must be defined before the Cassette is loaded into the Port ( From MES )
2) CIM PC Insert the defined key glass when the job change flag is detected
Machine Mode : Multi Product Mode
Glass Flow
Recipe A and A Key Glass : CST → Initial Cleaner → Oven → Block0 ( Route A )→ Block1 ( Route A ) → Block3 ( Route A ) → Block5 ( Route A ) → Block7 ( Route A ) → Block9 ( Route A ) → BlockA ( Route A ) → BlockC ( Route A )
Recipe B and B Key Glass : CST → Initial Cleaner → Oven → Block0 ( Route B )→ Block1 ( Route B ) → Block3 ( Route B ) → Block5 ( Route B ) → Block7 ( Route B ) → Block9 ( Route B ) → BlockA ( Route B ) → BlockC ( Route B )
Recipe A
Recipe B
Key A
Recipe
: Recipe A Flow
: Recipe B Flow
: Key A Recipe Flow
Key B
Recipe
: Key B Recipe Flow

## Slide 42: 2.1 Glass Flow
Cold Run Flow – All Machine Process Skip
CIM PC Mode : Cold Run Mode
Machine Mode : Cold Run Mode
1. Flow By Skip Recipe
- Flow by Cold run Recipe, All Machine Process Skip
2. Glass Flow
: CST → Cleaner → Oven( Process Unit By Pass ) → Block0 ~BlockC ( Process Unit By Pass ) → TM1(EN Line)
: Normal Glass
: Process Skip

## Slide 43: 2.1 Glass Flow
Cold Run Flow – Initial Cleaner Only
CIM PC Mode : Cold Run Mode
Machine Mode : Cleaner Only Cold Run Mode
1. Flow By Skip Recipe
- Flow by Initial Cleaner Only Cold run Recipe, Cleaner Machine Process Skip
2. Glass Flow
: Cassette -> Robot -> Initial Cleaner -> Robot -> Cassette
: Normal Glass
: Process Skip

## Slide 44: 2.1 Glass Flow
Dummy Flow - EN Dummy
CIM PC Mode : Normal Mode
Machine Mode : Normal Mode
1. Flow By Dummy Type of Job Data
- Dummy Type : PE-CVD ( TBD )
- Dummy Type : Inkjet ( TBD )
2. Glass Flow
: CST → Cleaner → Oven( Process Unit By Pass ) → Block0 ~BlockC ( Process Unit By Pass ) → TM1(EN Line)
: Normal Glass
: Process Skip

## Slide 45: 2.1 Glass Flow
IR Oven Reverse Flow
CIM PC Mode : Manual Mode
Machine Mode : Manual Mode
1. Flow By Machine Mode
  - This Mode Only Can use Semi Auto, If the block machine is down for a long time, the glass in the cooling buffer is returned back to the loader port.
2. Glass Flow
: Cooling Buffer -> Oven TM -> Initial Cleaner -> Robot -> Cassette
: Normal Glass
: Process Skip
Down

## Slide 46: 2.1 Glass Flow
Abnormal Flow – Force Clean out Mode
● This mode is used for the purpose of the Machine error/down state.
● The Machine should provide Clean Out Mode function on touch screen.
● The CIM PC control the robot for the glass transfer to the cassette.
Process Skip
Force Clean Out
Loading Stop/Start
Example of operation mode Switch on Touch Screen
Loading
Stop
Error
: Normal Glass
: Process Skip

## Slide 47: 2.1 Glass Flow
Abnormal Flow – Initial Cleaner Mismatching Recipe
CIM PC Mode : Manual Mode
Machine Mode : Manual Mode
1. Flow By Recipe
- If recipe of the inserted glass does not match, Glass Back to the Loader
2. Glass Flow
: CST → Robot → Cleaner → Robot → CST
: Normal Glass
: Process Skip
: Dummy Glass
Recipe Mismatching

## Slide 48: 2.3 Job Event
Job Event Flow ( Loader )
● Robot Arm Substrate Event
- When the substrate is loaded on robot arm, the indexer should report Arm Substrate Load Report
- When the substrate is unloaded from robot arm, the indexer should report Arm Substrate Unload Report
Loader
: Received Job Event
: Sent Out Job Event
: Stored Job Event
: Fetched Out Job Event
: Robot Arm Substrate Load Event
: Robot Arm Substrate Unload Event

## Slide 49: 2.3 Job Event
Job Event Flow (Machine)
: Received Job Event
: Sent Out Job Event
: Stored Job Event
: Fetched Out Job Event
: Robot Arm Substrate Load Event
: Robot Arm Substrate Unload Event
: Remove Job
Mask
Stock
Mask
Stock
CH#1
CH#2
Stage
Stage
Stage
Stage
Stage
Stage
Stage
Stage
EV
CA
EV
CB
EV
CE
EV
CD
EV
CE
Unit 2
Unit 1
Equipment
PT Unit
OC Cluster Unit
MET Unit
[Refer to Job Management in the PLC Communication Specification]

## Slide 50: 2.3 Job Event
Job Event Flow (Mask)
: Mask Stored Job Event
: Mask Fetched Out Job Event
Mask
Stock
Mask
Stock
Stage
Stage
Stage
Stage
Stage
Stage
Stage
Stage
EV
CA
EV
CB
EV
CE
EV
CD
EV
CE
OC Cluster Unit
MET Unit

## Slide 51: Sub Contents
Part 3. Equipment Operations
3.1 Equipment Processing Flag
3.2 Equipment Inspection Flag
3.3 Equipment State Rule
3.4 Job Data Validation
3.5 Equipment Specific Operation
3.6 Equipment Log Upload
3.7 DateTime Synchronization

## Slide 52: 3.1 Equipment Processing Flag
L2
L3
L4
L5
L6
L7
L8
L9
L10
L11
L12
If Glass is processed at the Equipment, Processing flag has to be set to “1” by Equipment
Local | L3 | L4 | L5 | L6 | L6 | L7 | L7 | L8 | L8 | L9 | L9 | L10 | L11 | L12 | L18 | L19
PLC Address (Word 1) | Bit0 | Bit1 | Bit2 | Bit3 | Bit4 | Bit5 | Bit6 | Bit7 | Bit8 | Bit9 | BitA | BitB | BitC | BitD | BitE | BitF
Equipment | ICLN | Oven | PC | EV1 | EV2 | EV3 | EV4 | EV5 | EV6 | EV7 | EV8 | EV9 | EVA | EVC | SE | LO
Processing Flag | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Local | L20 | L21 | L22 | L22 | L22 | L22 | L22 | L23 | L23 | L23 | L23 | L23 | L24 | L25 | L25 | L25
PLC Address (Word 2) | Bit0 | Bit1 | Bit2 | Bit3 | Bit4 | Bit5 | Bit6 | Bit7 | Bit8 | Bit9 | BitA | BitB | BitC | BitD | BitE | BitF
Equipment | OM | AOI1 | CVD1-PC01 | CVD1-PC02 | CVD1-PC03 | CVD1-PC04 | CVD1-PC05 | CVD2-PC01 | CVD2-PC02 | CVD2-PC03 | CVD2-PC04 | CVD2-PC05 | Cooling Buffer | IJP Print1 | IJP Print2 | UV1
Processing Flag | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 53: 3.1 Equipment Processing Flag
L2
L3
L4
L5
L6
L7
L8
L9
L10
L11
L12
Local | L25 | L25 | L25 | L25 | L25 | L27 | L29 | L30 | L30 | L30 | L30 | L30 | L31 | L31 | L31 | L31
PLC Address (Word 3) | Bit0 | Bit1 | Bit2 | Bit3 | Bit4 | Bit5 | Bit6 | Bit7 | Bit8 | Bit9 | BitA | BitB | BitC | BitD | BitE | BitF
Equipment | UV2 | UV3 | UV4 | UV5 | UV6 | IJP AOI | Aging Oven | CVD3-PC01 | CVD3-PC02 | CVD3-PC03 | CVD3-PC04 | CVD3-PC05 | CVD4-PC01 | CVD4-PC02 | CVD4-PC03 | CVD4-PC04
Processing Flag | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
If Glass is processed at the Equipment, Processing flag has to be set to “1” by Equipment
Local | L31 | L32 | L33 | L34 |  |  |  |  |  |  |  |  |  |  |  | 
PLC Address (Word 4) | Bit0 | Bit1 | Bit2 | Bit3 | Bit4 | Bit5 | Bit6 | Bit7 | Bit8 | Bit9 | BitA | BitB | BitC | BitD | BitE | BitF
Equipment | CVD4-PC05 | TFE SE | AOI3 | AOI4 |  |  |  |  |  |  |  |  |  |  |  | 
Processing Flag | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 54: 3.2 Equipment Inspection Flag
L2
L3
L4
L5
L6
L7
L8
L9
L10
L11
L12
Local | L18 | L19 | L20 | L21 | L27 | L32 | L33 | L34 |  | 
PLC Address (Processed Flag 01) | Bit0 | Bit1 | Bit2 | Bit3 | Bit4 | Bit5 | Bit6 | Bit8 | Bit9 | BitA
Equipment | SE | LO | OM | AOI1 | IJP AOI | TFE SE | AOI2 | AOI3 |  | 
Inspection Flag | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0
When Each Glass is transferred between machines, each machine checks the Inspection flag value and inspect Glass which inspection flag value is set “1”.

## Slide 55: 3.3 Equipment State Rule
Status Definitions for Each Equipment
[ Refer to Equipment Status in the Equipment Common Operation Scenario ]
Machine Status Definition
▶ IDLE : Status of process ended and waiting Instructions.
▶ RUN : Status of process started and working.
▶ BM : Status of unexpected problems, failures and Break-down Maintenance.
▶ PAUSE : Status of temporary stop. Stop means cycle-stop.
▶ PM : Status of preventive maintenance activities.
CIM-PC provides PM Button, also machine’s PM button is allowed. (Machine provide PM button on Touch Panel)
Job Change : Status of current equipment process product type is change
Machine provides Job Change button and report to CIM-PC ( Status=PM, Reason Code=Job Change)

## Slide 56: 3.4 Job Data Validation
Job Data Validation (Interlock)
1. Downstream machines check consistency and validation of job data.
2. if mismatching, missing or overlapping, interlock is activated.
3. If necessary, additional check could be added
Item | Type | Remark
Glass Size & Thickness | Validation | Check glass physical item
PPID | Validation | Recipe Check ● Registered in its own machine ● Mismatch to PPID on manual recipe change
 | Consistency | Missing Check ● Value missed
Glass ID, Glass Code | Validation | Duplication ● Check whether glass ID received already exists in its own machine
 | Consistency | Missing check ● Value missed
Glass Type | Validation | Glass Type (TFT, Dummy) Check

## Slide 57: 3.4 Job Data Validation
Operation
Case 1
1. Check Glass Data before Receiving Start Turn On
2. Down-Stream has to check the Process/Flow possibility.
If result is ‘fail’, Set operator call & send Alarm to CIM-PC
3. When Down-Stream’s Job change is finished Down-Stream unit retry 1. Sequence.
Case 2
1. Validation check is executed when upstream turns on send able.
2. If auto recipe change not supported, machine performs PPID mismatch check.
3. If PPID validation NG, then Machine raises alarm and stops transfer
4. Glass ID, glass type is optional and can be enable/disable on Down-Stream machine’s Screen.

## Slide 58: 3.4 Job Data Validation
Duplication
1. Consecutive same ID(or Glass Code)
2. Already exists in its own machine
3. If necessary, show glass list in order for last N glass.

## Slide 59: 3.5 Equipment Specific Operation
Loading Stop
CIM PC Mode : Abnormal Flow ( Cluster / Passage Down )
1. Glass Flow
Case1 : Oven Limit Over → Index Supply Stop
Case2 : Block0 Down → Glass Into Buffer(Oven) after Process → Port Limit Over(Oven) → Index Supply Stop
Case3 : BlockC Down → Block0 Load Lock Supply Stop → Glass Into Buffer(Oven) after Process → Port Limit Over(Oven) → Index Supply Stop
Case4 : Inspection Machine(LO or SE or OM) after Inspection completed then if Judge is NG,
Inspection Machine Request Loading stop give to Block 0 Machine
Loading Stop Request
Down
Limit
Over
Down
EN Inspection Machine
LO
SE
OM
CIM-PC
Loading Stop Request
Loading Stop Command

## Slide 60: 3.5 Equipment Specific Operation
Route Recipe
When Glass Loading completed on the Block 0 L/L, if necessary Block0 Machine Requests Route Recipe to CIM
In the case of using route recipe, This information should be defined before Glass Loading completed on the Block 0 L/L
Glass
EV Route Info Request

## Slide 61: 3.5 Equipment Specific Operation
Route Recipe – OK Case
EQ
EAS
MES
EV Route Recipe Info Request
EV Route Recipe Info Request Reply
Stored the Glass On Block L/L Stage
Received Job Report
Component in Unit
In the Case of using route recipe
EV Route Recipe Info Request
EV Route Recipe Info Send
Check the Route Recipe
Route Recipe Exist
Block 0 Machine Requests Route Recipe from CIM

## Slide 62: 3.5 Equipment Specific Operation
Route Recipe – NG Case
EQ
EAS
MES
EV Route Recipe Info Request
EV Route Recipe Info Request Reply
Stored the Glass On Block L/L Stage
Received Job Report
Component in Unit
In the Case of using route recipe
EV Route Recipe Info Request
EV Route Recipe Info Send
Check the Route Recipe
Route Recipe do not Exist
Alarm Report
Block 0 Machine Requests Route Recipe from CIM

## Slide 63: 3.5 Equipment Specific Operation
Dummy Glass Type
Dummy Glass Type
Dummy Glass Type
Tooling, Offset Normal monitor, PI, Key, Bare, TFE PE-CVD, TFE Inkjet
At, present , Test Center can provide EVEN Dummy Glass Of the eight kinds of CIM will reserve enough to guarantee follow up columns of increasing communication department and type, have been recorded into the normal dummy glass
Dummy Type | Value | Format
Normal | 1 | INT
Bare Dummy | 2 | INT
Tooling Dummy | 3 | INT
Offset Dummy | 4 | INT
PI Dummy | 5 | INT
Key Dummy | 6 | INT
TFE PE CVD Dummy | 7 | INT
TFE Inkjet Dummy | 8 | INT
TBD

## Slide 64: 3.5 Equipment Specific Operation
VCR Operation Scenario (Match - Just VCR Read Complete Report)
VCR Match I/F Scenario
Glass Code | Host Glass ID | VCR Glass ID
91001 | AA | AA
91002 | BB | BB
Machine
VCR stage
VCR
Glass Code : 91002
Glass ID : BB
Job Code : 91002
Received Job ID : BB
VCR Read Job ID : BB
EQP (E/I)
CIMPC
VCR Read Complete Report
- 91002 / BB
● Machine should support button to select “Modify Current Job ID by Read Job ID to Just Read Job ID” or “Job Data Request by Read
Job ID”
● Event flow:
If VCR Read ID is match with Received Job ID, machine reports VCR read complete report.
Step1

## Slide 65: 3.5 Equipment Specific Operation
VCR Operation Scenario(Mismatch - Modify Current Job ID by Read Job ID )
VCR Mismatch I/F Scenario
Glass Code | Host Glass ID | VCR Glass ID
91001 | AA | AA
91002 | BB | BB
Machine
VCR stage
VCR
Glass Code : 91002
Glass ID : BB
Job Code : 91002
Received Job ID : BB
VCR Read Job ID : AA
Job ID : AA
Machine update current glass Job ID to Read Job ID
EQP (E/I)
CIMPC
VCR Read Complete Report
- 91002 / AA
● Machine should support button to select “Modify Current Job ID by Read Job ID to Just Read Job ID” or “Job Data Request by Read
Job ID”
● If VCR Read ID is mismatch with Received Job ID. Machine should set alarm instantly
● Event flow:
Machine report VCR Read Complete Report to CIMPC
Machine report Job Data Change Report
Step1
Step2
Job data change Report
With Job ID AA

## Slide 66: 3.5 Equipment Specific Operation
Mask Load Port Management – Normal Scenario
EQ
EAS
MES
CST ID Reading OK
Slot Mapping Info
CST ID
Mask Cassette Load Complete
CST Validation Ok
Mask Cassette Data Request
Mask Cassette Data Request Reply
Mask CST Map Download
After Mask Cassette ID Reading
Cassette Validation OK
Port Status – In Use
Mask CST Map Download Reply
Cassette Process Start
Cassette Control Command
Port Status – Empty
Mask Cassette Load Completed On the Load Port

## Slide 67: 3.5 Equipment Specific Operation
Mask Load Port Management – Normal Scenario
EQ
EAS
MES
Fetched the Last Mask from the Load Port
Mask Fetched Report
Mask Out Report
Cassette Process End
Cassette Control Command
Cassette Process End
Port Status – Unload Ready
Port Status – Empty
Mask cassette is removed from the Load port
Fetched the first Mask from the Load Port
Cassette Process Start
Mask Fetched Report
Mask Out Report
Vent Complete
Start Vent
Cassette Unload Ready

## Slide 68: 3.5 Equipment Specific Operation
Mask Unload Port Management – Normal Scenario
EQ
EAS
MES
CST ID Reading OK
Slot Mapping Info
CST ID
Mask Cassette Load Complete
CST Validation Ok
Mask Cassette Data Request
Mask Cassette Data Request Reply
Mask CST Map Download
After Mask Cassette ID Reading
Cassette Validation OK
Port Status – In Use
Mask CST Map Download Reply
Cassette Process Start
Cassette Control Command
Port Status – Empty
Mask Cassette Load Completed On the Load Port

## Slide 69: 3.5 Equipment Specific Operation
Mask Unload Port Management – Normal Scenario
EQ
EAS
MES
Stored the Last Mask On the Unload Port
Mask Stored Report
Mask In Report
Cassette Process End
Cassette Control Command
Cassette Process End
Port Status – Unload Ready
Port Status – Empty
Mask cassette is removed from the Unload port
Stored the first Mask On the Unload Port
Cassette Process Start
Mask Stord Report
Mask In Report
Vent Complete
Start Vent
Cassette Unload Ready

## Slide 70: 3.5 Equipment Specific Operation
Mask Cassette Reload Command – OK Case
EQ
EAS
MES
CST ID Reading OK
Slot Mapping Info
Mask CST Map Download
After Mask Cassette ID Reading
Port Status – In Use
Mask CST Map Download Reply
Reload
Port Control Command
Port Status – Empty
CST ID Reading OK
Slot Mapping Info
++1 Lot Seq Number
Port Status – In Use
Port Control Command Reply
Return Code OK
Port Status – Unload Complete

## Slide 71: 3.5 Equipment Specific Operation
Mask Cassette Reload Command – NG Case
EQ
EAS
MES
CST ID Reading OK
Slot Mapping Info
Mask CST Map Download
After Mask Cassette ID Reading
Port Status – In Use
Mask CST Map Download Reply
Reload
Port Control Command
Port Control Command Reply
Return Code NG
Cassette Process Start
Cassette Control Command
After Cassette Process Start, Can’t use Reload

## Slide 72: 3.5 Equipment Specific Operation
Mask Load Port Management – Abnormal – Cancel by CIM
EQ
EAS
MES
Cassette Process Cancel
Cassette Control Command
Cassette Process End
Port Status – Unload Ready
Port Status – Empty
Mask cassette is removed from the Load port
In the case of before Cassette Process start
CIMPC Forced to Cancel
Vent Complete
Start Vent
Cassette Unload Ready

## Slide 73: 3.5 Equipment Specific Operation
Mask Load Port Management – Abnormal – Cancel by EQ
EQ
EAS
MES
Cassette Process End
Port Status – Unload Ready
Port Status – Empty
Mask cassette is removed from the Load port
In the case of before Cassette Process start
Operator Forced To Cancel or Indexer Forced to Cancel
Vent Complete
Start Vent
Cassette Unload Ready

## Slide 74: 3.5 Equipment Specific Operation
Mask Load Port Management – Abnormal – Abort by CIM
EQ
EAS
MES
Cassette Process Abort
Cassette Control Command
Cassette Process End
Port Status – Unload Ready
Port Status – Empty
Mask cassette is removed from the Load port
In the case of After Cassette Process start
CIMPC Forced to Abort
Vent Complete
Start Vent
Cassette Unload Ready

## Slide 75: 3.5 Equipment Specific Operation
Mask Load Port Management – Abnormal – Abort by EQ
EQ
EAS
MES
Cassette Process End
Port Status – Unload Ready
Port Status – Empty
Mask cassette is removed from the Load port
In the case of before Cassette Process start
Operator Forced To Abort or Indexer Forced to Abort
Vent Complete
Start Vent
Cassette Unload Ready

## Slide 76: 3.5 Equipment Specific Operation
Mask Offset Data Report
OM
EAS
Block
Mask Offset Data Report
Mask Offset Data Download
Completed OM Inspection
Block 1~C
Glass ID
Mask ID
Mask offset X, Y, Z
Mask Offset Data Download Result Download
Mask Offset Data Download Result
Block 1~C
TBD

## Slide 77: 3.5 Equipment Specific Operation
Mask Tooling Data Report
OM
EAS
Block
Mask Tooling Data Report
Mask Tooling Data Download
Completed OM Inspection
Block 1~C
Mask Tooling Data Download Result Download
Mask Tooling Data Download Result
Block 1~C
TBD

## Slide 78: 3.5 Equipment Specific Operation
Material(Mask) Special Data
Item Name | Description | Format | Word Points | Sub Items | Writable |  | 
 |  |  |  |  | CIM | LD | EQP
Loading Chamber ID | Loading Chamber ID & Stage | ASC | 10 | Download From MES ( Sub-Unit No) | W | W | 
Using Material Count | It is Only Used in the line which need Processing count Information by Material | INT | 1 | In Put The Mask Using Count by EQ(Timing : After Processed) |  |  | W
Mask OffSet X | Mask OffSet X | SINT | 2 | Download From MES | W | W | W
Mask OffSet Y | Mask OffSet Y | SINT | 2 | Download From MES | W | W | W
Mask OffSet T | Mask OffSet T | SINT | 2 | Download From MES | W | W | W
Mask Thickness | Mask Thickness | SINT | 2 | Download From MES | W | W | W
TBD

## Slide 79: Sub Contents
Part 4. Data Collection
4.1 SV(Status Variable)
4.2 DV(Process Data)
4.3 CV(Checked Variable)

## Slide 80
The status Variable data is machine Real Time Status Data (Machine Trace Data).
Machine writes SV Data into the word area by specified time cycle (10ms-500ms).
The detail SV data please reference to PLC map or SV data collection Excel.
4.1 SV(Status Variable)

## Slide 81: 4.2 DV(Process Data)
● Process Data has Processed Parameter values or inspection Result.
- Processing Time : it is actual processing time for a job in the equipment
● Kind of Process Data and Event Report Timing
- By Glass (Default) : The Process Data of each Glass should be reported before job sent to downstream equipment.
- By Lot (Default) : Machine should provide send DV Data either as By LOT using DV Type Option.

## Slide 82
The CV Data is the machine key parameter need BOE engineer to check every day, so need machine report to CIMPC so that BOE engineer can check this parameter in the office.
The contents of ‘CV Data’ is decided later after discussion.
The Maximum size of CV Data Report area and Timing can be changed after discussing.
The detail CV data please reference to PLC map or CV data collection Excel.
4.3 CV(Checked Variable)
CIM-PC
Machine
Repeat Count Set
Count=N
CV Report Stop
CV Report Time Change Command (count=N)
CV Report Time Change Command Reply
CV Data Report#1
Stop Report
[Normal Scenario – Stop by RepeatCount]
CV Data Report#2
...
CV Data Report#N
CIM-PC
Machine
Repeat Count Set
Count=N
CV Report Time Change Command (count=N)
CV Report Time Change Command Reply
CV Data Report#1
Stop Report
[AbNormal Scenario – Stop by CIMPC]
CV Data Report#2
...
CV Report Time Change Command (count=0)
CV Report Time Change Command Reply

## Slide 83: Sub Contents
Part 5. Open Issue
5.1 Open Issue List

## Slide 84: 5.1 Open Issue List